## Slide 1
Simulating KGD: GF65nm SAR ADC
https://github.com/USCPOSH/AMS_KGD/tree/master/ADC/SAR_ADC/GF65LPe
IMPORTANT NOTES REGARDING RULE FILES FOR THE LAYOUT:
The runset, DRC, LVS, PEX Calibre files are not included in the repository.
It is left to the details of the user's installation of Calibre to set these up.
There is nothing design specific to get Calibre DRC and PEX going.

## Slide 2
Simulating KGD: GF65nm SAR ADC
1) Copy the library to /workarea_GF55
https://github.com/USCPOSH/AMS_KGD/tree/master/ADC/SAR_ADC/GF65LPe
Testbenches may be found in April 2019 release folder.

## Slide 3
2) Add the library to cadence search path
https://github.com/USCPOSH/AMS_KGD/tree/master/ADC/SAR_ADC/GF65LPe
Simulating KGD: GF65nm SAR ADC
Open cds.lib in /workarea_GF55
Add the line shown below

## Slide 4
https://github.com/USCPOSH/AMS_KGD/tree/master/ADC/SAR_ADC/GF65LPe
Simulating KGD: GF65nm SAR ADC
3) Open design and find testbenches under corresponding categories
Location of testbenches

## Slide 5
https://github.com/USCPOSH/AMS_KGD/tree/master/ADC/SAR_ADC/GF65LPe
Simulating KGD: GF65nm SAR ADC
4) Change the path of model file
Open ADE L
Click Setup -> Model Libraries
Find the location of your model file
5) Click simulation button!