## Slide 1
Multiple fingers cannot be set for MOSFET when using the PTM model; multiplier can be used instead.
Write simulator lang = spice at top of the .pm (model) file to simulate.
* downloading requires registration with academic email.
Hyperlinked Summary of Predictive Models
Developer | Layout availability | Device type | Device flavors | Technology node (nm) | Latest Release Version
Nanoscale Integration & Modeling group @ ASU (PTM) | No | Bulk CMOS | - | 130, 90, 65 | 1.0
 |  |  | HP (High-Performance) | 45, 32, 22, 16 | 2.1
 |  |  | LP (Low-Power) | 45, 32, 22, 16 | 2.1
 |  | Multi-gate (FinFET) | HP (High-Performance) | NMOS: 20, 16, 14, 10, 7 | -
 |  |  |  | PMOS: 20, 16, 14, 10, 7 | 
 |  |  | LSTP (Low-Standby Power) | NMOS: 20, 16, 14, 10, 7 | -
 |  |  |  | PMOS: 20, 16, 14, 10, 7 | 
ASU + ARM collaboration (ASAP)* | Yes | Multi-gate (FinFET) | 4 threshold voltage, 3 corner | 7 | 1.6